## Comparing Gravitational, Electrostatic and Magnetic Fields

| Experimental results and equations | Field concept |
| --- | --- |
| (a) Two masses exert a force on each other. Force, F = | Either mass is the source of a gravitational field and the other mass experiences a force due to that field. At any point, the gravitational field strength g (N kg-1) is the force acting on a one kg mass placed at that point. |
| (b) Two stationary electric charges exert a force on each other. Force, F = | Either charge is the source of an electrostatic field and the other charge experiences a force due to that field. At any point, the electric field strength E (N C-1) is the force acting on +1 C of charge placed at that point. |
| (c) Two parallel current-carrying wires exert a force on each other. Force for one metre of wire, F is given by F = The force between such wires is due to the movement of charge carriers, the current. | Either current-carrying wire is the source of a magnetic field and the other current-carrying wire experiences a force due to that field. At any point, the magnetic induction B is given by B = . |

The unification of electricity and magnetism by J C Maxwell is stated on page 1, where c  =  .

# Text boxes

F

r

+ Q1

+ Q2

+ Q2

+ Q1

I2 experiences the magnetic induction B of I1

B

I1

I2

I1

r

F

F

m1

m2

r

F

F

m1

m2

+ Q1

+ Q2

+ Q2

+ Q1

r

F

F

F

r

I1

I2

I1

B

I2 experiences the magnetic induction B of I1