Electric Potential Tutorial

  - The unit of field strength is __________________.

  - The unit of electric potential is ________________.

  - The absolute electric potential at a point is the work done moving a unit charge ______________.

  - In practise the electric potential is the work done moving a unit charge from ____ _____________________

  - Electric field lines meet an equipotential surface at ___________.

- A hollow metal sphere of radius 5 cm has a charge of +20 nC.

  - What is the field strength at the outer surface?

  - What is the potential at the outer surface?

  - What is the field strength at the centre?

  - What is the potential at the centre?

  - Illustrate graphically how the field strength varies from the centre of the sphere to a distance of 20 cm.

  - Similarly illustrate how the potential varies from the centre of the sphere to a distance of 20 cm.

  - Calculate the acceleration of an electron placed at a distance of 20 cm from the centre of the sphere.

  - What will happen to the acceleration as it moves nearer to the sphere?

  - How much work will be done on the electron as it moves from a distance of 20 cm from the centre of the sphere onto the surface of the sphere?

- A series of electrons is emitted from the cathode of an electron gun. The anode is at a potential of +400 V to the cathode and is 10 mm from it.

  - Calculate the velocity of one of the electrons as it passes through the hole at the centre of the anode.

  - Will a relativistic correction be required?

  - What is the field strength between the plates?

  - What is the acceleration of the electron?

  - If the anode was moved to 20 mm from the cathode but maintained at the same potential difference would the acceleration or the final velocity change?

- An oil drop of 4 x 10-12 g is midway between two horizontal parallel plates, which are 2 mm apart. The upper is at a potential difference of +200 V relative to the lower one. The oil drop has a charge of 4 surplus electrons.

  - Calculate the field strength between the plates.

  - Show and name diagrammatically the forces acting on the oil drop.

  - What will be the acceleration of the oil drop?

  - At what potential difference on the plates would the oil drop be balanced?