## Slide 1: LOCKERBIE ACADEMY TRANSPORT UNIT SPEED
S1-S3 Road Safety & PHYSICS

## Slide 2: LOCKERBIE ACADEMY TRANSPORT UNIT
Notes: All of these road signs relate to Physics in some way, whether mention of speed, force, acceleration or other physics terms. We are going to use the topic of road safety to teach you about MECHANICS. DYNAMICS and KINEMATICS (there are some big words for you to find out about)
We will use the upside down car, which we made up as our logo for this topic. It is meant to represent no road accidents here as we know about the Physics behind driving and we should know how to be safe.

## Slide 3: LOCKERBIE ACADEMY TRANSPORT UNIT
We plan to find out and understand about the following terms
P distance
P displacement
P speed
P velocity
P instantaneous/ average/ uniform/ speed
P time & at rest
Notes: We are going to learn about some vital and basic parts of Physics through a unit on ROAD SAFETY (catchy name needed over to Mr Bowles). We will be looking at road accidents and safe driving. If you have a problem with this YOU MUST tell your teacher who will ensure that you are not given work that makes you upset.
We plan to find out and understand about the following terms
P distance
P displacement
P speed
P velocity
P instantaneous speed
P forces, including weight, and friction
P time
P acceleration
If we have time we might mention momentum.

## Slide 4: Speed, Distance & Time
S1 Physics Transport
Back to mind map

## Slide 5: Reading the stopclock
The stopclock display can be a bit confusing.
A number that looks like this: 0:0234 means 2.34 seconds.
Start & Stop
Reset

## Slide 7
Speed
v
d
t
Examples using the Speed Formula (Showing full working):
1. The sprinter ran 100 metres in 10 seconds. What was his speed ?

## Slide 8: LOCKERBIE ACADEMY TRANSPORT UNIT
In Physics we show the divide by sign as a line and say “over”
where v=speed, d=distance and t=time
Notes: We must be careful as we can look at different speeds. During a journey from Lockerbie Car Park to Tesco car park we would not travel at the same speed (Possibly go through the journey or part of it on Google maps
http://maps.google.co.uk/maps?q=google+street+map+DG11+2AT&oe=utf-8&cr=countryUK|countryGB&um=1&ie=UTF-8&sa=N&hl=en&tab=wl
We would have to slow down over the speed bumps and stop if there were people crossing the (PROPER NAME FOR LIGHT CONTROLLED CROSSING) but at some points we might get close to 30 mph but unlikely as it is a busy route unless we went via ***** Therefore over this journey we can look at 2 types of speed- our instantaneous speed and our average speed. Can anyone think what these terms mean?

## Slide 9: The SPEED OF MY CAR
Your Team Challenge
Each member of your team must drive the course with their vehicle. They must NOT stray off the track or they have to return to the start.
Notes: VEHICLE- add to wordbank

## Slide 10: The SPEED OF MY CAR
Your Team Challenge
You must time how long it takes each member to complete the journey and measure the distance travelled along the track.
Record each team member’s time and calculate the average speed for each journey.
Notes: VEHICLE- add to wordbank

## Slide 11: LOCKERBIE ACADEMY TRANSPORT UNIT

## Slide 12: LOCKERBIE ACADEMY TRANSPORT UNIT

## Slide 13: YOUR TASK.
TASK
Working in teams you need to:
Measure the DISTANCE that the car will travel along the pre-defined course.
Record this value on your worksheet.
Time how long each person in the group takes to complete the course.
Record this value on your worksheet
Record as tally marks on your worksheet every time each person in the group leaves the track

## Slide 14: LOCKERBIE ACADEMY TRANSPORT UNIT
Vehicle
A thing used for transporting people or goods, especially on land, such as a car, truck, or cart.
WORDBANK

## Slide 15: LOCKERBIE ACADEMY TRANSPORT UNIT
Distance- is how far you have travelled. It is another name for length. It is measured in metres or during our road safety topic miles.
Time- is how long your journey took. It is measured in seconds or during our road safety topic hours.
WORDBANK

## Slide 16: Additional Notes- For Printing only if repeat measurements required
To find the average speed from your results
Find the average time for the 3 runs (if the race was run 3 times)
  Do this by adding the times for the three runs in the calculator, PUSH the = button on the calculator and then divide this answer by 3 (as there were 3 runs). Add this number to your table where it says average time)
Find the speed using the formula
  Speed = distance  time
Add this value of speed to your table.
DO NOT give your average speed to more than 1 decimal place unless the value is very small.

## Slide 17: LOCKERBIE ACADEMY TRANSPORT UNIT
Speed – how far you travel every second.
OR
Speed is the distance travelled in unit time.
In the lab our distances are measured in metres and our time is measured in seconds so our units of speed would be metres per second.
In road safety we look at miles travelled every hour or miles per hour.
WORDBANK
Notes: In Physics this would be metres travelled every second so our units would be metres per second. In road safety we look at miles travelled every hour or miles per hour. To work this out you must use the formula

## Slide 18: LOCKERBIE ACADEMY TRANSPORT UNIT
At rest- in Physics we use this term to mean not moving. We can also say the object is stationary.
It is not the same word as pens and pencils which are stationery!
WORDBANK

## Slide 19: Let’s try some examples
Matt’s time for the course was 00:01:55. The course was 1.78m. What was Matt’s speed around the course?

## Slide 20: AND THE WINNING TEAM IS
FIXING your calculators
FIX allows you to fix how many figures after the decimal point should be displayed i.e. it fixes the number of decimal places you quote a value to. This is really useful if you suffer from calculator diarrhoea, but be careful you could end up with zero!

## Slide 21: AND THE WINNING TEAM IS
Calculate the average speed for each of your team drivers.

## Slide 22: AND THE WINNING TEAM IS
And the winner is………

## Slide 23: Let’s try some examples
Let’s try some more examples of speed distance and time and then in your groups we can do the domino challenge.
But first let’s look at how to set out equations

## Slide 24: HOW TO LAY OUT EQUATIONS IN PHYSICS
http://www.youtube.com/watch?v=u7akhlAS5Ck
Check before you play!

## Slide 25: IESSUU
Information
Equation
Substitution
Solution
Units
Underline
& remember no SECS in PHYSICS

## Slide 26
2. The Porsche travelled at 40 m/s for 2 minutes. How far did it go ?
speed=40m/s
Time = 2 minutes (260)= 120 second
=4800 m
Information
Equation
Substitution
Solution
Units
Underline

## Slide 27: Let’s try some examples
Work out the average speeds for the following journeys. Make sure you set out your working in the same way as the example above.
1. A boat travels 30 km in 3 hours.
2. A tractor drives 18 km in 6 hours.
3. A frog jumps 25 metres in 5 seconds.
(Take care with the units.)
4. A plane flies 600 km in 3 hours.

## Slide 28: Let’s try some examples
1. A boat travels 30 km in 3 hours.
d= 30km
t= 3h
v=?
I
E
S
S
U
U

## Slide 29: Let’s try some examples
2. A tractor drives 18 km in 6 hours.
d= 18km
t= 6h
v=?
E
S
S
U
U
I

## Slide 30: Let’s try some examples
3. A frog jumps 25 metres in 5 seconds.
(Take care with the units.)
d= 25m
t= 5s
v=?
v=5m/s
E
S
S
U
U
I

## Slide 31: Let’s try some examples
4. A plane flies 600 km in 3 hours.
d= 600km
t= 3h
v=?
E
S
S
U
U
I

## Slide 32: IN YOUR MATHS SECTION WRITE OUT THE FOLLOWING EXAMPLE
Tony walks 40m in 30s what is his average speed?
v=?, t=30s, d=40m
speed=distance/time
speed=40/30 = 1m/s

## Slide 33: IN YOUR MATHS SECTION WRITE OUT THE FOLLOWING EXAMPLE
You could write 1.3m/s, 1.33m/s or 1.333m/s and get the mark. If you write 1.33. m/s or 1 1/3 m/s or 1.333333m/s you lose the mark for the answer! This is because you have used TOO MANY SIGNIFICANT FIGURES.
Mrs Hargreaves calls this “calculator diarrhoea”! and you can FIX it!!!!

## Slide 34
Speed Dominoes

## Slide 35: THE POST VAN AND AVERAGE SPEED.
Post Office
Post Box
Church
Shop
Library
200 m / 25 s
450 m / 60 s
400 m / 32 s
350 m / 35 s
750 m / 120 s
900 m / 45 s

## Slide 36
Journey | Average Speed
Post Office  Post Box | 
Post Office  Church | 
Post Box  Church | 
Library  Shop  Church | 
Post Office  Post Box  Church | 
Post Office  Church  Shop  Library | 

## Slide 37: INSTANTANEOUS Speed
S1 Physics Transport
Back to mind map

## Slide 38: LOCKERBIE ACADEMY TRANSPORT UNIT
Instantaneous speed is the speed at which you are travelling over a very short distance. It is measured in metres per second or miles per hour.
WORDBANK

## Slide 39: Instantaneous Velocity
The instantaneous speed for an object is its speed at a particular point in time. For example, a police speed camera measures the instantaneous velocity of the car.
Length of object
Light gate measures time to pass
Ramp
WORDBANK

## Slide 40: LOCKERBIE ACADEMY TRANSPORT UNIT
A speedometer is a gauge that measures and displays the instantaneous speed of a land vehicle.
Notes: Instantaneous speed is the speed at which you are travelling over a very short distance. It is measured in metres per second or miles per hour.

## Slide 41: INSTANTANEOUS SPEED
Speed Cameras in D&G

## Slide 45: Instantaneous Velocity
Instantaneous speed is difficult to measure.
WHY?
Let’s try it!

## Slide 46
An investigation to measure reaction time and calculate stopping distances
Using the Reaction Timer box you will find out:
Your reaction time.
How your reaction time changes if you are chatting or texting.
You will calculate stopping distances for different speeds.
Image: Wikipedia: This work is licensed under the Creative Commons Attribution 2.0 License.

## Slide 47: MEASURING INSTANTANEOUS Speed
S1 Physics Transport
Back to mind map

## Slide 48: MEASURING INSTANTANEOUS SPEED- get the instruction sheets
USING A STOPWATCH
What you need:
Model vehicle, ruler, chalk, stopclock, instruction sheet

## Slide 49: MEASURING INSTANTANEOUS SPEED USING A STOPWATCH
What you need
Model vehicle, ruler, chalk, stopclock.
What to do
Mark one chalk line on the bench. (Don’t forget to rub it out when you have finished!).
Measure the length of the model vehicle. Record this in your jotter.

## Slide 50: MEASURING INSTANTANEOUS SPEED USING A STOPWATCH
Start the stopclock when the front edge of the vehicle reaches the chalk line.
Stop the stopclock when the end of the car reaches the chalk line.
Note the time from the stopclock in your jotter.
Calculate the speed using the formula:

## Slide 51: MEASURING INSTANTANEOUS Speed (let’s not worry about reaction time!)
S1 Physics Transport
Back to mind map

## Slide 52: MEASURING INSTANTANEOUS SPEED- get the instruction sheets
USING ALBA & LIGHT GATES
What you need:
Model vehicle, ruler, mask, lightgates + laptop, instruction sheet

## Slide 53: Instantaneous Velocity
Instantaneous speed
Length of object
Light gate measures time to pass
Ramp
One way is to use a light gate. The length of the object divided by the time it takes to pass gives its instantaneous speed.

## Slide 54: MEASURING YOUR INSTANTANEOUS SPEED
GROUP TASK- back to the PLAYMATS!
We need to know the
1. length of your vehicle or the mask on top.
2. the time for the vehicle to pass through the light gates
3. the instantaneous speed of the vehicle as it goes round the roundabout (or alternative)

## Slide 55: YOUR TASK.
Working in teams you need to:
Using the ALBA package record the instantaneous speed of the vehicle at the specific place in the track (see the additional worksheet)
ALBA-MOTION
Introduction to SPEED

## Slide 58: LOCKERBIE ACADEMY TRANSPORT UNIT
“Speed camera”
Measure instantaneous speed here

## Slide 59: LOCKERBIE ACADEMY TRANSPORT UNIT
“Speed camera”
Measure instantaneous speed here

## Slide 64: REACTION TIME
S1 Physics Transport
Back to mind map

## Slide 65: Let’s measure YOUR REACTIONS
Sheep Dash
MEASURING REACTION TIME USING A COMPUTER
MEASURING REACTION TIME USING A RULER
Collect the helpsheet for the instructions on how to find
REACTION TIME using a RULER.
On the internet try some of the experiments for finding your reaction time.
5 min road test
Red dot yellow dot
Notes: Experiment sheets provided

## Slide 66: REACTION TIME
To measure your reaction time you will need a 30 cm ruler, an instruction sheet and a partner.
MEASURING REACTION TIME USING A RULER
Notes: MEASURING REACTION TIME USING A RULER
To measure your reaction time you will need a 30 cm ruler and a partner. What to do
  i. Your partner holds a ruler at the top. The 0 cm mark should be pointing towards the ground, the 30 cm mark should be pointing towards the ceiling.
  ii. Place your finger and thumb either side of the 0 cm mark, but do not hold the ruler.
  iii. Your partner should let the ruler go, at the same time you should try to grab the ruler between your finger and thumb.
  iv. Record the distance the ruler has fallen in your jotter, from the 0 cm to where you are holding it. The distance must be recorded in metres.
  v. Repeat this five times.
  vi. Your partner now tries to grab the ruler as you let it go.
To find the time:
  i. Find the average distance the ruler dropped before you grabbed it.
  ii. Multiply your average distance by 0.2 and then square root your answer.
To do this using your calculator
Average reaction time =
average distance × 0.2 =√=
(metres)
What to do
  i. Your partner holds a ruler at the top. The 0 cm mark should be pointing towards the ground, the 30 cm mark should be pointing towards the ceiling.
  ii. Place your finger and thumb either side of the 0 cm mark, but do not hold the ruler.
  iii. Your partner should let the ruler go, at the same time you should try to grab the ruler between your finger and thumb.
  iv. Record the distance the ruler has fallen in your jotter, from the 0 cm to where you are holding it. The distance must be recorded in metres.
  v. Repeat this five times.
  vi. Your partner now tries to grab the ruler as you let it go.
To find the time:
  i. Find the average distance the ruler dropped before you grabbed it.
  ii. Multiply your average distance by 0.2 and then square root your answer.
To do this using your calculator
Average reaction time =
average distance × 0.2 =√=
(metres)

## Slide 67: LOCKERBIE ACADEMY TRANSPORT UNIT
At rest- in Physics we use this term to mean not moving. We can also say the object is stationary.
It is not the same word as pens and pencils which are stationery!
WORDBANK

## Slide 68: STOPPING DISTANCE
The STOPPING DISTANCE of a car is made up of TWO parts
THINKING DISTANCE
BRAKING DISTANCE
Thinking distance is the distance a car will travel in the time it takes you to react to the situation.
The distance the car will travel as the brakes are applied

## Slide 69: LOCKERBIE ACADEMY TRANSPORT UNIT
Stopping distance = thinking + braking
distance distance
Stopping distance the distance it takes a car to stop.
WORDBANK

## Slide 70: LOCKERBIE ACADEMY TRANSPORT UNIT
WORDBANK
the distance that the car moves whilst braking.
braking distance
the distance moved whilst you are reacting to the hazard.
thinking distance

## Slide 72
An investigation to measure reaction time and calculate stopping distances
Using the Reaction Timer box you will find out:
Your reaction time.
How your reaction time changes if you are chatting or texting.
You will calculate stopping distances for different speeds.
Image: Wikipedia: This work is licensed under the Creative Commons Attribution 2.0 License.

## Slide 73
By, Hannah, Charlotte, Robert and Kieran + Emma, Sophie, Phoebe, Sweez & Faye edited by Mrs H
[Original photo credit: lonecellotheory]

## Slide 74: What chicken is for?
To get you to learn about the stopping distances of cars and lorries
To be aware of road safety.
To appreciate stopping distances.
Braking in different weather conditions.

## Slide 75: Equipment
Car controls
(reaction timer)
A driver
Measuring tape
Mario kart wheel
People to be chickens

## Slide 76: What is it.
Chicken run is an experiment that tests your reaction time and people’s appreciation of stopping distances.
You choose
    weather condition
    speed
    driver ability
    driver distractions

## Slide 77: The Winner
is the person closest to stopping position of “the car” without being “hit”
Not these then!

## Slide 78: Rules
Drive carefully
Do not break Mario kart wheel
Don’t have your hand hovering over the stop button
Don’t look at the light whilst you’re driving
Think of the control box as a proper car
DO NOT GET HURT

## Slide 81: Cross Curricular Links
Literacy
Q: Why did the chicken run across the road? A: There was a car coming. Q: Why did the chicken cross the road halfway? A: She wanted to lay it on the line. Q: Why did the rubber chicken cross the road? A: She wanted to stretch her legs. Q: Why did the Roman chicken cross the road? A: She was afraid someone would caesar! Q: Why did the chicken cross the road? A: To prove to the possum it could actually be done!

## Slide 82: Cross Curricular Links
Literacy
http://www.miketheheadlesschicken.org/story.php
Numeracy
Speed, distance, measuring, unit conversions
H&W

## Slide 83: UNIFORM Speed
S1 Physics Transport
Back to mind map

## Slide 84: LOCKERBIE ACADEMY TRANSPORT UNIT
Uniform Speed
Sometimes through the whole journey your speed will not change. This could be because you have cruise controls on. We would say that your speed is UNIFORM when your speed isn’t changing. It remains constant.

## Slide 85: LOCKERBIE ACADEMY TRANSPORT UNIT
Uniform Speed
When your speed is uniform we mean that your speed isn’t changing. It remains constant.
WORDBANK

## Slide 86: Uniform speed
Do you think people often travel at a uniform speed?
Discuss times when the speed might be uniform and when it might not be uniform.
WHY?

## Slide 87: LOCKERBIE ACADEMY TRANSPORT UNIT

## Slide 88: SPEED AND ROAD SAFETY
Speed is given as the MAIN cause of FATAL ACCIDENTS on Scotland’s Roads
Road Accident Report

## Slide 89: SPEED AND ROAD SAFETY
Causes of road traffic accidents
In Great Britain, data collected6 about road traffic accidents in 1999 to 2002 examined the factors involved in each accident. Excessive speed was the most common contributory factor in fatal accidents, playing a part in 28% of all fatal accidents examined in the trial. Careless, thoughtless or reckless behaviour was next, being a contributory factor in 21% of all fatal accidents examined.
In accidents resulting in any severity of casualty, inattention was the most common contributory factor, found in 25% of all accidents examined in the trial. Failing to judge another person's path or speed was the next most common contributory factor, playing a part in 23% of all accidents examined.
road_traffic_accident.html

## Slide 90: THINKING TASK!- More CARS less deaths- WHY?
Crash Figures

## Slide 92: ADVANCED QUESTIONS
Questions – Speed
1. What is the speed of a motorbike if it travels 100 metres in 2.5 seconds?
2. what is the speed of a rocket if it can move 32 kilometres in 4 seconds?
3. At what speed in m/s is a skateboarder moving if he can skate 6 kilometres in 10 minutes?
4. A red Ferrari zooms over 500 metres in 4 seconds. What is its speed?
5. How long would it take a snail to slither 20 metres at 5 metres per hour?