# 2000 General Paper

- B – 1 ampere			[1]

- A – 				[1]

- D – computer			(1)

- E – increase the amplitude of an electrical signal		[1]

5.a.	FM radio, air traffic control	(1)

b.	300 – 3 000 MHz		(1)

6.a.i. sound  electrical		[1]

ii. electrical  sound		[1]

b.i. 3x108 m/s			[1]

ii. 	The signals pass through the air as a radio wave			(2)

c.	PA – conveys information to many people at the same time OR one way communication		(1)

2way – allows two way communication OR allows communication in private	(1)

7.a.	tuner,  TV tube		[1]

b.	aerial				[1]

c.	provides the energy for the

amplifiers			[1]

8.	Hazards are : too many plugs in one adapter,  poorly repaired flex,  stereo in bathroom,  flex under door

Dangers : risk of electrocution/death,  tripping on flex,  overheating causing a fire etc.			(4)

9.   a.	I =  =  = 0.05 A 	[½,½,1]

b.i					[1]

ii.	A – 230 V			[1]

B – step down transformer	[1]

iii.	Mains – alternating current	(1)

Battery – direct current	(1)

10.  a.	bell – collects (and amplifies) the sounds from the patients chest

tubing – carries the sounds from the bell to the earpieces,  small volume to reduce sound loss against the walls

earpieces – fit snugly into the doctor’s ears cutting out any background noise				[3]

b.	To reduce sound loss / cut out background noise		(1)

11.  a.	laser light			(1)

b.	ultra violet			(1)

c.	X-rays				(1)

12.  a.

| Device | Component |
| --- | --- |
| Automatic night light | LDR |
| Automatic fire alarm | thermistor |
| Time delay for pedestrian crossing | capacitor |

[3 x 1]

b. i.	transistor			[1]

ii.	automatic switch		(1)

c.	R reduces the current through the LED OR reduces the voltage across the LED OR protects the LED.	[1]

13.  a.	You need the length of the card (l) and the time that the light gate is blocked for (t),  the instantaneous speed will be v = 	(1 for each meas, 1 for equation)

b.  	a = =

= 0.4 m/s2 		(½,½,1)

c.	NOT CORRECT because the time on the stopwatch is shorter so the human reaction time is a greater proportion.

CORRECT because the time taken to pass through the light gate is longer so the reading error on the electronic timer will be more accurate.	(2)

14.  a.	w = mg = 20 000 x 10

= 200 000 N 		[½,½,1]

b.	Balanced forces mean the train will be moving at constant speed (Newton’s 1st Law)			[1]

c. i.	EP = mgh = 20 000 x 10 x 300

= 60 000 000 J

= 6 x 107 J = 60 MJ	(½,½,1)

ii.	P =  =  = 125 000 W

= 1.25 x 105 W = 125 kW 	[½,½,1]

iii.	The power will be greater because more is needed when the train is accelerating and also to overcome the effects of friction		(1)

15 a.

| Fossil fuels | Other energy sources |
| --- | --- |
| Coal | Nuclear |
| Oil | Hydroelectric |
| Gas | Biomass |

(3)

b.  	Total %age fossil fuels = 24 + 32 + 18  			   = 74 %   	[1]

c.	Fossil fuels are a finite resource and are running out. 		(1)

d.	Wind,  wave,  tidal,  solar,  etc.   [1]

16.  a.

(3 x 1)

b.					coil

[2]

magnet			iron core

17.  a.	length of time = year – 1991

e.g. in year 2000 = 2000 – 1991

= 9 years	   (1)

- Planet,  galaxy,  star (not sun) 	   [3]

(1 sun to Jupiter,  1 Jupiter to Earth,  no arrows no marks)

18.	curved,  acceleration,  force of gravity,  neither				[4 x 1]

Total marks			KU	[40]

PS	(40)

## Grade 3 -  28   (N.B. half marks

Grade 4 -  20         are rounded up)

Grade 5 -  16

Grade 7 -  15

# 2001 General Paper

1.	B - tuner			[1]

2.	C - loudspeaker		(1)

3.	A – blue, green, red		[1]

4.	A – 0 N			(1)

5.	E – kinetic energy is transferred to heat					(1)

6.						[1]

7. a. i.	f =  =  = 2 Hz [½,½,1]

ii.	 =  =  = 1.5 m [½,½,1]

iii.	 = 2 x 1.5 = 3 m/s 	[½,½,1]

b. i.	top to bottom = 15 – 13 = 2

amplitude =  =  = 1 cm 	[1,1]

ii.	The wave has lost energy	(1)

8. a. i.

| Stage | How transmitted |  |
| --- | --- | --- |
| 1 | sound | (1) |
| 2 | microwave | (1) |
| 3 | light | (1) |
| 4 | electrical | [1] |

ii.	Stage 1 - sound		(1)

b.

[1 – reflection, 1 – focus]

c.

(1 – TIR, 1 – st. lines)

9.   a.

|  | Lamp1 | Lamp2 | Lamp3 |  |
| --- | --- | --- | --- | --- |
| Current (A) | 0.3 | 0.3 | 0.3 | (1) |
| Voltage (V) | 12 | 12 | 12 | [1] |

ii.

|  | Lamp1 | Lamp2 | Lamp3 |  |
| --- | --- | --- | --- | --- |
| Current (A) | 0.1 | 0.1 | 0.1 | [1] |
| Voltage (V) | 4 | 4 | 4 | (1) |

b. i	Circuit 1			(1)

ii.	Any suitable plug in 		(1)

10.  a.	230 V				[1]

b.	Can be operated independently OR

If one blows the rest stay on OR

Same voltage across them	(2 x 1)

c. i.	Power = no of lamps x power of each

= 8 x 800 = 6 400 W

= 6.4 kW	(½,½,½,½)

- A – kWh = 6.4 x 3

= 19.2 kWh	(½,½)

B – cost = kWh x rate = 19.2 x 5

= 96 pence	(½,½,1)

d.	MCB, circuit breaker etc.	[1]

11.a.i.	P – its range includes the melting point of ice			(1,1)

ii.	Q – more accurate		(1,1)

b.	give it a shake,  place in patients mouth etc, allow to get to body temp,  take reading		[½,½,½,½]

c.	Reading is above normal body temperature,  patient has a fever. [1,1]

12.a.i.	infra red detector		(1)

ii.	light dependant resistor (LDR) (1)

b. i.	A - AND gate  		[1]

B - 				[2]

| Input P | Input Q | Output |
| --- | --- | --- |
| 0 | 0 | 0 |
| 0 | 1 | 0 |
| 1 | 0 | 0 |
| 1 | 1 | 1 |

ii.	AND gate			(1)

13.  a.	force,  10 N			[2 x 1]

b. i	P – the maximum force it can measure is 2 N which is not enough for the 10 N block.			(1, 1)

ii.	R – would not be accurate as the weight is less than one division on the balance.			(1)

14. a.i.	 = 4180 x 120 x (34 – 18)

= 4180 x 120 x 16

= 8 025 600 J       [1 – temp, ½,½,1]

ii.	t =  =

= 40 128 s	[½, ½, 1]

b.	Heat energy is being lost to the surroundings		(1)

15.a. i.	Water is pumped from a lower reservoir to a higher one,  using surplus electricity / at times of low demand on the grid.		[1, 1]

ii.	More efficient,  recycles water,  less water required.	[1]

b.	 = 1 x 10 x 400

= 4 000 J		[½, ½, 1]

c. i.	The top label is the CORE

The left label is the PRIMARY COIL

The right label is the SECONDARY COIL			(3 x 1)

ii.	 =

= 165 000 turns	[½, ½, 1]

iii.	Reduces power/energy loss	[1]

16.a. i.	Europa			(1)

ii.	Jupiter			(1)

iii.	Sun			(1)

b. i.	eyepiece,  magnify		(½, ½)

ii.	objective,  collect light	(½, ½)

Total marks			KU	[40]

PS	(40)

## Grade 3 -  28   (N.B. half marks

Grade 4 -  20         are rounded up)

Grade 5 -  16

Grade 7 -  15